## Slide 1: ROS - Lesson 12
Teaching Assistant: Roi Yehoshua
roiyeho@gmail.com
Fall 2014

## Slide 2: Agenda
Run navigation stack with Gazebo
Send goals to robots in Gazebo
Robotic coverage problem

## Slide 3: Setting Up Navigation Stack
Copy the package send_goals into a new package called gazebo_navigation
Change the name of the package in package.xml, CMakeLists.txt and move_base.xml
Remove stage_config subdirectory
Copy the launch file random_walk.launch from the launch directory in gazebo_random_walk package
  Rename it to gazebo_navigation.launch
Add the following lines to the launch file

## Slide 4: gazebo_navigation package

## Slide 5: Maps Directory
We will run the navigation stack with a given map
Create a maps directory in your package and copy willow-full.pgm file into it
  $ roscd navigation_stage/stage_config/maps
  $ cp willow-full.pgm ~/catkin_ws/src/gazebo_navigation/maps

## Slide 6: Map’s Pose in Gazebo and ROS
By default the origin of the map is different in Gazebo and ROS
In Gazebo the origin is by default at the center of the map while in ROS it is at the lower-left corner
The map’s pose in Gazebo can be changed by adjusting its model in Gazebo’s world file
For that purpose, we first need to copy the world’s file into our package

## Slide 7: Change Map’s Pose in Gazebo
Create worlds directory in your package
Copy willowgarage.world file from gazebo’s worlds directory to worlds directory of your package
Now edit the world’s file to adjust the model’s pose
The pose parameter consists of 6 values: <x y z r p y>
  Angles are specified in degrees
  $ roscd gazebo_navigation/worlds
  $ cp /usr/share/gazebo-2.2/worlds/willowgarage.world .

## Slide 8: willowgarage.world
  <?xml version="1.0" ?>
  <sdf version="1.4">
  <world name="default">
  <include>
  <uri>model://ground_plane</uri>
  </include>
  <include>
  <uri>model://sun</uri>
  </include>
  <include>
  <uri>model://willowgarage</uri>
  <pose>-3 54 0 0 0 30</pose>
  </include>
  </world>
  </sdf>

## Slide 9: Change Map’s Pose in Gazebo
We also need to change the launch file of Gazebo’s world to launch our own version of the world file
First copy willowgarage_world.launch from gazebo_ros package to the launch directory of your package
Now edit this file
  $ roscd gazebo_ros/launch
  $ cp willowgarage_world.launch ~/catkin_ws/src/gazebo_navigation/launch

## Slide 10: willowgarage_world.launch
  <launch>
  <!-- We resume the logic in empty_world.launch, changing only the name of the world to be launched -->
  <include file="$(find gazebo_ros)/launch/empty_world.launch">
  <arg name="world_name" value="$(find gazebo_navigation)/worlds/willowgarage.world"/>
  <arg name="paused" value="false"/>
  <arg name="use_sim_time" value="true"/>
  <arg name="gui" value="true"/>
  <arg name="headless" value="false"/>
  <arg name="debug" value="false"/>
  </include>
  </launch>

## Slide 11: TF Tree
For the navigation stack to work properly, the robot needs to publish the following transformations:
map
robotX/odom
robotX/base_link
robotX/laser_link
published by the localization system
published by Gazebo’s driver controller
published by static tf defined in your launch file

## Slide 12: Gazebo position_3d Controller
First, you need to make Gazebo publish the robot’s position to ROS
This can be done with the position_3d controller
Add the following to the URDF file:
<plugin name="p3d_base_controller" filename="libgazebo_ros_p3d.so">
<alwaysOn>true</alwaysOn>
<updateRate>100.0</updateRate>
<bodyName>base_link</bodyName>
<topicName>base_pose_ground_truth</topicName>
<gaussianNoise>0</gaussianNoise>
<frameName>/map</frameName>
<xyzOffsets>0 0 0</xyzOffsets>
<rpyOffsets>0 0 0</rpyOffsets>
</plugin>

## Slide 13: Laser Scanner Controller
The gazebo model, written in URDF, makes use of an Hokuyo laser scanner through the libgazebo_ros_laser.so plugin
The frameName property of the plugin specifies the TF frame that corresponds to the laser link
Change it to laser_link
<plugin name="gazebo_ros_laser_controller" filename="libgazebo_ros_laser.so">
<topicName>base_scan</topicName>
<frameName>laser_link</frameName>
</plugin>

## Slide 14: Laser Scanner Controller
However, the laser plugin doesn't automatically publishes a transform from base_link to the frame that you specified in the file (laser_link)
Thus we need to manually specify a static transform publisher between the laser_link and base_link frames
We will add this publisher to the launch file

## Slide 15: gazebo_navigation.launch
<launch>
<param name="/use_sim_time" value="true" />
<!-- Launch world -->
<include file="$(find gazebo_ros)/launch/willowgarage_world.launch"/> <arg name="init_pose" value="-x 20 -y 15 -z 0"/>
<!--<param name="robot_description" textfile="$(find r2d2_description)/urdf/r2d2.urdf"/>-->
<param name="robot_description" textfile="$(find lizi_description)/urdf/lizi.urdf"/>
<!-- Spawn robot's model -->
<node name="spawn_urdf" pkg="gazebo_ros" type="spawn_model" args="$(arg init_pose) -urdf -param robot_description -model my_robot" output="screen"/>
<node name="joint_state_publisher" pkg="joint_state_publisher" type="joint_state_publisher"/>
<node pkg="robot_state_publisher" type="robot_state_publisher" name="robot_state_publisher" output="screen"/>
<node pkg="tf" type="static_transform_publisher" name="laser_link_broadcaster" args="0 0 1 0 0 0 base_link laser_link 100" />
<!-- Run navigation stack with AMCL -->
<node name="map_server" pkg="map_server" type="map_server" args="$(find gazebo_navigation)/maps/willow-full.png 0.1"/>
<include file="$(find gazebo_navigation)/move_base_config/move_base.xml"/>
<include file="$(find gazebo_navigation)/move_base_config/amcl_node.xml"/>
<param name="amcl/initial_pose_x" value="20" />
<param name="amcl/initial_pose_y" value="15" />
<node name="rviz" pkg="rviz" type="rviz" args="-d $(find gazebo_navigation)/single_robot.rviz" />
</launch>

## Slide 16: Running the Navigation Stack
Now we are ready to run the navigation stack
  $ roslaunch gazebo_navigation gazebo_navigation.launch

## Slide 17: Gazebo

## Slide 18: rviz

## Slide 19: Set Navigation Goal
Open rviz menu – Tool Properties
Change the topic name for the 2D Nav Goal according to the robot that you want to activate:

## Slide 20: Set Navigation Goal

## Slide 21: Following the Global Plan

## Slide 22: Final Pose

## Slide 23: Final Pose in Gazebo

## Slide 24: Robotic Coverage Problem
In robotic coverage, a robot is required to visit every part of a given area using the most efficient path possible
Coverage has many applications in a many domains, such as search and rescue, mapping, and surveillance.
The general coverage problem is analogous to the TSP problem, which is NP-complete

## Slide 25: Grid-Based Methods
Assume that the environment can be decomposed into a collection of uniform grid cells
Each cell is either occupied or free

## Slide 26: STC Algorithm
Gabrieli and Rimon [2001]
Assumption: the robot is equipped with a square shaped tool of size D (the coverage tool)
Switch to coarse grid, each cell of size 4D
Create Spanning Tree (ST) on the coarse grid
  Using Prim or Kruskal’s algorithms
The robot walks along the ST, creating a Hamiltonian cycle visiting all cells of the fine grid.
The algorithm finds the optimal coverage path in linear time

## Slide 27: STC Execution Example
Taken from Gabriely and Rimon, 2001

## Slide 28: Moving with Odometry Data
As we have learned, you can publish Twist messages to the /cmd_vel topic to make the robot move in the environment
However, calculating the exact number of commands needed to send to the robot to make it move only one cell in the grid can be error-prone
Moreover, the accuracy and reliability of this process depend on the current condition of the robot and its internal sensors
  For example, if the robot just started moving, the first velocity command will take some time to take effect

## Slide 29: Moving with Odometry Data
Rather than guessing distances and angles based on time and speed, we can monitor the robot's position and orientation as reported by the transform between the /odom and /base_footprint frames (odometry data)
This way we can be more precise about moving our robot

## Slide 30: Moving with Odometry Data
void moveToRightCell()
{
// Set the forward linear speed to 0.2 meters per second
float linearSpeed = 0.2f;
geometry_msgs::Twist move_msg;
move_msg.linear.x = linearSpeed;
// Set the target cell
int targetCell = currCell.first + 1;
// How fast will we update the robot's movement?
ros::Rate rate(20);
// Move until we reach the target cell
while (ros::ok() && currCell.first < targetCell)
{
cmdVelPublisher.publish(move_msg);
rate.sleep();
getRobotCurrentPosition();
showCurrentPosition();
}
// Stop the robot (in case the last command is still active)
geometry_msgs::Twist stop_msg;
cmdVelPublisher.publish(stop_msg);
sleep(1);
}

## Slide 31: Final Project
Implement the STC algorithm using ROS + Gazebo
More details can be found at: http://u.cs.biu.ac.il/~yehoshr1/89-685/FinalProject/FinalProject.html