## Slide 1: ROS - Lesson 4
Teaching Assistant: Roi Yehoshua
roiyeho@gmail.com
Fall 2014

## Slide 2: Agenda
Stage simulator
Reading laser sensor data
Writing a simple walker
Your first assignment

## Slide 3: ROS Stage Simulator
http://wiki.ros.org/simulator_stage
A 2D simulator that provides a virtual world populated by mobile robots, along with various objects for the robots to sense and manipulate

## Slide 4: Run Stage with an existing world file
Stage is already installed with ROS Indigo
Stage ships with some example world files, including one that puts an Erratic-like robot in a Willow Garage-like environment
To run it with an existing world file
Browsing the stage window should show up 2 little squares: a red square which is a red box and a blue square which is the erratic robot
  rosrun stage_ros stageros `rospack find stage_ros`/world/willow-erratic.world

## Slide 5: Run Stage with an existing world file
Click on the stage window and press R to see the perspective view.

## Slide 6: Stage World Files
The world file is a description of the world that Stage must simulate.
It describes robots, sensors, actuators, moveable and immovable objects.
Sample world files can be found at the /world subdirectory in ros_stage package

## Slide 7: World File Format
The basic syntactic features of the world file format: comments, entities and properties
The define statement can be used to define new types of entities.
  define myrobot position (player() laser() )
Entities have properties, indicated using name value pairs
  myrobot (name "robot1" port 6665 pose [1 1 0])
    This entry creates a position device named "robot1" attached to port 6665, with initial position (1, 1) and orientation of 0

## Slide 8: Stage World File Example
define block model
(
size [0.5 0.5 0.75]
gui_nose 0
)
define topurg ranger
(
sensor(
range_max 30.0
fov 270.25
samples 1081
)
# generic model properties
color "black"
size [ 0.05 0.05 0.1 ]
)
define pr2 position
(
size [0.65 0.65 0.25]
origin [-0.05 0 0 0]
gui_nose 1
drive "omni"
topurg(pose [ 0.275 0.000 0 0.000 ])
)

## Slide 9: Stage World File Example
define floorplan model
(
# sombre, sensible, artistic
color "gray30"
# most maps will need a bounding box
boundary 1
gui_nose 0
gui_grid 0
gui_outline 0
gripper_return 0
fiducial_return 0
ranger_return 1
)
# set the resolution of the underlying raytrace model in meters
resolution 0.02
interval_sim 100 # simulation timestep in milliseconds
window
(
size [ 745.000 448.000 ]
rotate [ 0.000 -1.560 ]
scale 18.806
)

## Slide 10: Stage World File Example
# load an environment bitmap
floorplan
(
name "willow"
bitmap "../maps/willow-full-0.05.pgm"
size [58.25 47.25 1.0]
pose [ -23.625 29.125 0 90.000 ]
)
# throw in a robot
pr2( pose [ -28.610 13.562 0 99.786 ] name "pr2" color "blue")
block( pose [ -25.062 12.909 0 180.000 ] color "red")
block( pose [ -25.062 12.909 0 180.000 ] color "red")
block( pose [ -25.062 12.909 0 180.000 ] color "red“)

## Slide 11: Move the robot around
You have a simulated robot - let's make it move
An easy way to do this is keyboard-based teleoperation
For keyboard teleoperation, you need to get a package called teleop_twist_keyboard which is part of the brown_remotelab stack
  http://wiki.ros.org/brown_remotelab

## Slide 12: Installing External ROS Packages
Create a directory for downloaded packages
  For example, ~/ros/stacks
Edit ROS_PACKAGE_PATH in your .bashrc to include your own ros stacks directory
Check the package out from the SVN:
Compile the package
  export ROS_PACKAGE_PATH=~/ros/stacks:${ROS_PACKAGE_PATH}
  $ cd ~/ros/stacks
  $ svn co https://brown-ros-pkg.googlecode.com/svn/trunk/distribution/brown_remotelab
  $ rosmake brown_remotelab

## Slide 13: Move the robot around
Now run teleop_twist_keyboard:
You should see console output that gives you the key-to-control mapping, something like this:
  Hold down any of those keys to drive the robot. E.g., to drive forward, hold down the i key.
  $ rosrun teleop_twist_keyboard teleop_twist_keyboard.py

## Slide 14: Move the robot around

## Slide 15: Stage Published Topics
The stage simulator publishes several topics
See what topics are available using rostopic list
You can use rostopic echo -n 1 to look at an instance of the data on one of the topics

## Slide 16: Odometry Messages

## Slide 17: A Stopper Node
We will create a node called stopper that will make the robot move forward until it detects an obstacle in front of it
We will use the laser sensor data to achieve this
Create a new package called my_stage
  $ cd ~/catkin_ws/src
  $ catkin_create_pkg my_stage std_msgs rospy roscpp

## Slide 18: Laser Scanner

## Slide 19: Hokuyo Laser
A common laser sensor used in robotics
  http://www.hokuyo-aut.jp/02sensor/07scanner/urg_04lx.html

## Slide 20: Hokuyo Laser

## Slide 21: Laser Scan Data
In Stage Click D (or choose View > Data) to see the laser data on the map

## Slide 22: Laser Scan Data
Laser data is published to the topic /base_scan
The message type that used to send information of the laser is sensor_msgs/LaserScan
You can see the structure of the message using
Note that Stage produces perfect laser scans
  Real robots and real lasers exhibit noise that Stage isn't simulating
$rosmsg show sensor_msgs/LaserScan

## Slide 23: LaserScan Message
http://docs.ros.org/api/sensor_msgs/html/msg/LaserScan.html

## Slide 24: LaserScan Message
Example of a laser scan message from Stage simulator:

## Slide 25: A Stopper Node
In Eclipse under the package’s src directory add a new class named Stopper
  This will create Stopper.h and Stopper.cpp
Add a source file run_stopper.cpp
  This will contain the main function

## Slide 26: Stopper.h
#include "ros/ros.h"
#include "sensor_msgs/LaserScan.h"
class Stopper {
public:
// Tunable parameters
const static double FORWARD_SPEED_MPS = 0.5;
const static double MIN_SCAN_ANGLE_RAD = -30.0/180*M_PI;
const static double MAX_SCAN_ANGLE_RAD = +30.0/180*M_PI;
const static float MIN_PROXIMITY_RANGE_M = 0.5; // Should be smaller than sensor_msgs::LaserScan::range_max
Stopper();
void startMoving();
private:
ros::NodeHandle node;
ros::Publisher commandPub; // Publisher to the robot's velocity command topic
ros::Subscriber laserSub; // Subscriber to the robot's laser scan topic
bool keepMoving; // Indicates whether the robot should continue moving
void moveForward();
void scanCallback(const sensor_msgs::LaserScan::ConstPtr& scan);
};

## Slide 27: Stopper.cpp (1)
#include "Stopper.h"
#include "geometry_msgs/Twist.h"
Stopper::Stopper()
{
keepMoving = true;
// Advertise a new publisher for the simulated robot's velocity command topic
commandPub = node.advertise<geometry_msgs::Twist>("cmd_vel", 10);
// Subscribe to the simulated robot's laser scan topic
laserSub = node.subscribe("base_scan", 1, &Stopper::scanCallback, this);
}
// Send a velocity command
void Stopper::moveForward() {
geometry_msgs::Twist msg; // The default constructor will set all commands to 0
msg.linear.x = FORWARD_SPEED_MPS;
commandPub.publish(msg);
};

## Slide 28: Stopper.cpp (2)
// Process the incoming laser scan message
void Stopper::scanCallback(const sensor_msgs::LaserScan::ConstPtr& scan)
{
// Find the closest range between the defined minimum and maximum angles
int minIndex = ceil((MIN_SCAN_ANGLE_RAD - scan->angle_min) / scan->angle_increment);
int maxIndex = floor((MAX_SCAN_ANGLE_RAD - scan->angle_min) / scan->angle_increment);
float closestRange = scan->ranges[minIndex];
for (int currIndex = minIndex + 1; currIndex <= maxIndex; currIndex++) {
if (scan->ranges[currIndex] < closestRange) {
closestRange = scan->ranges[currIndex];
}
}
ROS_INFO_STREAM("Closest range: " << closestRange);
if (closestRange < MIN_PROXIMITY_RANGE_M) {
ROS_INFO("Stop!");
keepMoving = false;
}
}

## Slide 29: Stopper.cpp (3)
void Stopper::startMoving()
{
ros::Rate rate(10);
ROS_INFO("Start moving");
// Keep spinning loop until user presses Ctrl+C or the robot got too close to an obstacle
while (ros::ok() && keepMoving) {
moveForward();
ros::spinOnce(); // Need to call this function often to allow ROS to process incoming messages
rate.sleep();
}
}

## Slide 30: run_stopper.cpp
#include "Stopper.h"
int main(int argc, char **argv) {
// Initiate new ROS node named "stopper"
ros::init(argc, argv, "stopper");
// Create new stopper object
Stopper stopper;
// Start the movement
stopper.startMoving();
return 0;
};

## Slide 31: CMakeLists.txt
Edit the following lines in CMakeLists.txt:
  cmake_minimum_required(VERSION 2.8.3)
  project(my_stage)
  …
  ## Declare a cpp executable
  add_executable(stopper src/Stopper.cpp src/run_stopper.cpp)
  ## Specify libraries to link a library or executable target against
  target_link_libraries(stopper ${catkin_LIBRARIES})

## Slide 32: Stopper Output

## Slide 33: Launch File
Launch file for launching both the Stage simulator and the stopper node:
To run the launch file use:
$ roslaunch my_stage my_stage.launch
  <launch>
  <node name="stage" pkg="stage_ros" type="stageros" args="$(find stage_ros)/world/willow-erratic.world"/>
  <node name="stopper" pkg="my_stage" type="stopper" output="screen"/>
  </launch>

## Slide 34: Launch File

## Slide 35: Assignment #1
In your first assignment you will implement a simple walker algorithm much like a Roomba robot vaccum cleaner
Read assignment details at http://u.cs.biu.ac.il/~yehoshr1/89-685/assignment1/assignment1.html